## Slide 1
CNH DATA COLLECTION PROJECT
From sunflower seeds to a weight estimate
What can make the weight wrong, how we control it, how easy it is for the user, and what the data cost
Hadi Nasooti and Jia | KU Leuven | 26 October 2026
Notes: Title. We estimate the weight of a pile of sunflower seeds from one phone photo. Today: the variables that make the weight wrong and how we handle them, how it works for the user, and a business case for the data.

## Slide 2
The story in one slide
OVERVIEW
What can make the weight wrong?
We listed 32 variables and measured most of them (the untested ones are marked). Camera height, phone and person are removed by the fixed scale.
Is it easy for the user?
One photo from any height, no ruler, no settings. The app gives one light with one sentence: what to change if the photo is not good.
Is the data worth its cost?
10 piles (about 2 hours, about 100 euro) give ±9.4 % with the marker sheet. We have 17 piles: ±8.7 %. Jia's 9 test piles: 9 of 9 inside.
1.2 %
what the photo itself adds: one pile, 16 photos, 2 persons, 2 phones, 2 heights
53 of 53
of our normal photos get a green light; all 6 problem photos orange
±8.7 %
95 % range for one photo, 17 piles, about 3.6 hours of work
Notes: CNH asked three questions in the class of 19 October. Here are the three short answers; the rest of the talk shows the evidence. Range = 95 % prediction interval: about 19 of 20 true weights fall inside.

## Slide 3
How we collect one sample
METHOD
1 Weigh
TARE, then scoop the seeds; write the weight
2 Spread
On white paper, no seed touches another
3 Markers
Two printed 50 mm squares next to the seeds
4 Photo
Straight down, any height, 1x camera, 2 photos
5 Weigh again
TARE, all seeds back; this weight is used
Each rule comes from a problem we measured
TARE every time: without it the scale read 1 g too high (coin test).
No seed touches another: touching seeds gave 16 to 19 % fewer seeds.
Markers in the photo: without them the count depends on height and phone.
Nothing else in the photo: false boxes on writing and a ruler.
Never crop: cropping cut seeds at the edge.
Written down so someone else can follow it
Procedure (version 3) in the repository, PROCEDURE.md.
Tested: Jia repeated it on 9 new piles with another phone (slide 10).
The same rules are now inside the app as instructions and checks (slide 11).
Notes: Our procedure in five steps. Every rule answers a problem we saw in our own data. The procedure is written so CNH can follow it from the text alone; Jia tested that.

## Slide 4
What data we collected
DATASET
17 Oct
Pilot
1 pile of 25 g, 3 batches of 200 hand-counted seeds
19 Oct
Hadi P01 to P08
10 to 24 g, 24 photos (iPhone 15 Pro)
19 Oct
Gauge R&R
1 untouched pile, 17 photos: 2 persons, 2 phones, 2 heights
20 Oct
Jia T4-01 to T4-04
11 to 23 g, 8 photos (iPhone 14): repeat of the procedure
21 Oct
Jia P09 to P13
27 to 34 g, 10 photos: bigger piles
17 piles
10 to 34 g, all weighed
59 photos
counted by the detector
4.3 hours
of photo time in all sessions
P14 and P15 dropped
A bigger sample is split into two photos; after 17 piles one more pile adds almost nothing.
Notes: Five sessions. The Gauge R&R is one pile that nobody touches, photographed by both of us with both phones at two heights: it measures the photo error alone. Jia's piles are the test of the procedure.

## Slide 5
What can make the weight wrong, and our fix
VARIABLES
Variable | Effect we measured | How we handle it
Camera height | Same pile: 112 to 292 seeds without fixed scale, 283 to 298 with it | Fixed scale from the markers (before counting)
Phone resolution | 12 MP: -18 %, 8 MP: -43 % without fixed scale; about 2 % with it | Fixed scale (before counting)
Person, phone model | Same pile: 0.0 % and +0.3 % | Written procedure; nothing else needed
Seeds touching | 16 to 19 % fewer seeds | Procedure; orange light (after counting)
Phone tilted | Markers 9.5 % different in size: count only -2.2 % | Orange light above 5 % (after counting)
Marker cut off | -12.6 % without a scale | Seeds used as the ruler: +1.5 % (orange light)
Other objects (ruler, notes) | +5 to +28.5 % when all boxes are counted | Count sunflower boxes only
Shadows | -2.3 to +2.0 %: no effect shown | Procedure: do not block the light
Kitchen scale, 1 g steps | 1.7 % (2.9 % at 10 g) | Piles of 10 g or more; TARE
All 32 variables, how each was measured and what the user sees: docs/group/VARIABLES.md
Notes: The top variables. For each one: what we measured, and where we handle it: in the procedure, before counting (the fixed scale), or after counting (the light in the app). The full table has 32 rows, including the ones we could not test, like background colour and blur.

## Slide 6
The biggest step: one fixed scale for every photo
CALIBRATION
Chart: Same untouched pile, 16 photos: seeds counted
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Photo as taken | 206 | 112 | 262 | 234 | 228 | 213 | 234 | 255 | 259 | 290 | 289 | 290 | 272 | 268 | 286 | 292
Fixed scale (0.110 mm per pixel) | 288 | 289 | 292 | 287 | 287 | 298 | 289 | 287 | 288 | 294 | 290 | 290 | 289 | 290 | 291 | 283
Without the fixed scale
112 to 292 seeds on the same pile (spread 18.6 %). A higher photo or a phone with fewer pixels makes seeds smaller, and the detector misses them.
With the fixed scale
283 to 298 seeds (spread 1.2 %). The two 50 mm markers give mm per pixel; every photo is resized to 0.110 mm per pixel before counting. Built into the app.
Notes: This chart is the strongest result. Orange bars: the same pile counted on the photo as it was taken: anything from 112 to 292 seeds. Green bars: the same photos after resizing with the markers: 283 to 298. So camera height and phone no longer matter.

## Slide 7
Gauge R&R: the photo is not the problem
REPEATABILITY
One untouched pile, 2 persons x 2 phones x 2 heights, 17 photos (16 with the markers found)
Person
0.0 %
Jia minus Hadi; 95 % CI -1.4 to +1.5 %
Phone
+0.3 %
iPhone 14 minus iPhone 15 Pro; CI -1.1 to +1.7 %
Height
0.0 %
high minus normal; CI -1.3 to +1.3 %
Same photo again
1.3 %
typical change when the same person takes the photo again
What it means
The 8 groups (person x phone x height) differ no more than two photos in the same group (analysis of variance, p = 0.81). The photo adds about 1 %; piles differ by about 4 %.
Limits
One pile; heights written as normal or high, not measured. It does not test how a person spreads the seeds: Jia's repeat does that (slide 10).
Notes: CI = confidence interval: the range where the true difference lies with 95 % certainty. All three intervals include zero and are small, so person, phone and height do not change the count in a way we can detect. Analysis of variance compares the differences between the 8 groups with the differences inside each group; p = 0.81 means the group differences are what chance alone would give.

## Slide 8
Which feature tells the weight (task 2)
MODEL
Feature (Hadi's 8 piles) | r | 95 % range of r | Spread
Count of all boxes | 0.990 | 0.950 to 0.999 | 3.7 %
Count of sunflower boxes | 0.989 | 0.945 to 0.999 | 4.0 %
Box area of sunflower boxes, mm² | 0.985 | 0.930 to 0.999 | 5.4 %
Box area of sunflower boxes, pixels | 0.900 | 0.635 to 0.990 | 11.6 %
Mean box area, pixels | -0.271 | -0.984 to 0.753 | 35.7 %
r = correlation with the weight (1 = perfect line). Spread = how much grams per unit of the feature varies between piles; lower is better. How many piles we need: slide 13.
Chosen model
weight = number of sunflower boxes x 0.05336 g per seed (all 17 piles)
Why sunflower boxes only
It ignores the false boxes on writing, notes and the ruler.
Still best for Jia
Her photos: count r 0.994, box area 0.988.
Notes: We compared five features. The count of sunflower boxes is as good as the count of all boxes, and safer when other objects are in the photo. Area in pixels is poor because it changes with height. The same ranking holds on Jia's photos.

## Slide 9
How sure are we? (task 3)
UNCERTAINTY
Chart: Error budget, 17 piles (relative standard deviation, %)
| Total spread between piles | Kitchen scale (1 g steps) | Photo (mean of 2 photos) | Remainder: seeds and the rest
Relative error (%) | 3.97 | 1.73 | 0.93 | 3.45
Relative standard deviation = typical error as % of the weight. Parts add as squares: 3.97² = 1.73² + 0.93² + 3.45². The remainder is found by subtraction, not measured.
The range for one photo
range = t x s x sqrt(1 + 1/n)
= 2.12 x 3.97 % x 1.03 = ±8.7 %
s = spread, n = 17 piles, t = factor for few piles. 19 of 20 true weights should fall inside.
What it tells us
The photo is no longer the main error (0.9 %).
The rest sits in the seeds and the 1 g kitchen scale: a 0.01 g scale would show the seed-to-seed part.
Notes: Top-down, the 17 piles spread 3.97 %. Bottom-up, the scale step is 1.73 % (calculated) and the photo 0.93 % (measured in the Gauge R&R). What is left, 3.45 %, is a remainder found by subtraction: seed weight and errors we cannot separate. With t for 17 piles the range for one photo is plus or minus 8.7 %. Be honest about task 3: because the remainder is found by subtraction, top-down and bottom-up agree by construction. The one stage we measured independently is the detector: on 3 hand-counted batches of 200 seeds it was off by about 1 % (photos without markers, scale estimated).

## Slide 10
Does it hold for another person? (task 4)
TEST
Chart: Jia's 9 piles, model of 19 Oct (Hadi's 8 piles), not refitted
| T4-01 | T4-02 | T4-03 | T4-04 | P09 | P10 | P11 | P12 | P13
Error of the prediction (%) | -2.5 | 4.3 | -3.4 | -5.7 | -7.4 | -2.3 | 2 | 2.4 | 0.7
Bound +10 % | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
Bound -10 % | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10
9 of 9 inside the bounds
Average error -1.3 %, mean absolute error 3.4 %.
Also for the bigger piles (27 to 34 g) that Hadi never weighed.
Same grams per seed?
Jia +1.5 % (95 % CI -2.7 to +5.7 %): no difference found.
Honest note
T4-02: 14 g before, 12 g after the photos. With the before weight: 8 of 9 inside.
Notes: Jia followed only the written procedure, with her own phone. We applied Hadi's model of 19 October without changing it. All 9 piles fall inside plus or minus 10 %. That supports the bounds; 9 piles cannot prove them. After this test we used all 17 piles together.

## Slide 11
For the user: one photo, one light, one sentence
USER
On the screen before the photo
1. Spread the seeds on white paper, no seed touching another.
2. Put the marker sheet next to them. No sheet? The app still works, with a wider range.
3. Phone flat, straight above, any height.
4. Too many seeds? Split the sample.
No ruler, no measured height, no settings.
Light and range are two things
The light says if the photo follows the rules. The range says how exact the ruler is (17 piles): ±8.7 % with the marker sheet, ±9.4 % with the seeds.
12.1 g (11.0 to 13.1 g) Green
Good photo. Real weight: 12 g.
11.9 g (10.9 to 12.9 g) Orange
Seeds too close together: spread them so that no seed touches another, and take the photo again. Real weight: 14 g.
15.8 g (14.3 to 17.3 g) Orange
No marker found: the size was estimated from the seeds, so the range is wider. Put the marker sheet fully in the photo for a more precise result.
no weight Red (example)
No seeds found: check that the seeds are in the photo.
The first three are real results from the app. Limits from our own photos: all 53 normal photos green, all 6 known problem photos orange.
Notes: The app never just gives a number. It shows a light. Green: trust it. Orange: you get a weight, and one sentence on how to make a better photo: seeds too close, phone tilted, too many seeds, or no marker. Red: no weight. The second example is a photo where the seeds touched: the true weight was 14 g, and the app warns. Every limit comes from our own photos.

## Slide 12
No marker? The seeds become the ruler
USER
 | Marker sheet | Seeds as ruler
What the user needs | Printed sheet | Nothing extra
Count compared with the marker count | reference | -1.0 % on average (worst ‑5.6 %)
Range for one photo, 17 piles | ±8.7 % | ±9.4 %
Same pile, 16 photos (Gauge R&R) | 1.16 % | 1.22 %
Photo where the markers were cut off | -12.6 % | +1.5 %
How it works
Typical seed length (11.25 mm, measured once with the markers) / median box length in the photo = mm per pixel. Count once, resize, count again.
Next step for a real app
Accept any object of known size: coin, bank card (85.60 x 53.98 mm) or an A4 sheet.
Order: marker, then coin or card, then the seeds. Not tested yet.
Limit
The seed length must be known per crop and seed lot. It varied 11.25 to 11.88 mm between our sessions; on Jia's piles the seeds-as-ruler error was -2.9 % on average. A 5 % wrong seed length changed the count by about 1.4 % (controlled test, 4 photos).
Notes: A real user will not print our sheet. So when there is no marker, the app measures the seeds themselves and uses them as the ruler. Tested on all our photos: the range grows only from 8.7 to 9.4 %. A coin or a bank card would be better than the seeds, because their size is exactly known; that is the next step.

## Slide 13
Business case: what one more pile buys
BUSINESS CASE
Chart: 95 % range for one photo against the number of piles
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Range for one photo (±%) | 19.72 | 14.13 | 12.07 | 11.02 | 10.38 | 9.96 | 9.65 | 9.42 | 9.24 | 9.09 | 8.98 | 8.88 | 8.79 | 8.72 | 8.66 | 8.61 | 8.56 | 8.51 | 8.48 | 8.44 | 8.41 | 8.38 | 8.36 | 8.33 | 8.31 | 8.29 | 8.27 | 8.25 | 8.24 | 8.22 | 8.21 | 8.19 | 8.18 | 8.17 | 8.16 | 8.15 | 8.14 | 8.13 | 8.12 | 8.11 | 8.1 | 8.1 | 8.09 | 8.08 | 8.08 | 8.07 | 8.06 | 8.06
8 piles ±10.0 % | 10 piles ±9.4 % | 17 piles ±8.7 % | never below ±7.8 % (1 g kitchen scale, one seed lot). With only 17 piles the true value at 17 could be ±6.4 to ±13.2 %.
Cost of one pile
10.20 euro (12.7 min, piles of 10 to 24 g) to 17.35 euro (21.6 min, 27 to 34 g). Example rate 48.2 euro per hour, Eurostat 2024, Belgium.
Stop rule: 10 piles
From 10 piles on, one more pile narrows the range by less than 0.2 percentage points: 0.1 point costs 5.67 euro or more, and the price keeps rising.
Spend the money elsewhere
A 0.01 g scale, and a new calibration (about 10 piles, about 100 euro) per seed lot. An extra photo of the same pile costs 0.25 euro but helps little.
Notes: Task 2 asked how many samples we need; this is the answer with costs. Each pile took 12.7 minutes, about 10 euro at an example labour rate; bigger piles took longer. The range shrinks fast up to about 10 piles, then hardly moves. A percentage point is the difference between two percentages, for example from 9.4 to 9.2 % is 0.2 points. Our stop rule: stop when one more pile buys less than 0.2 points. We kept Jia's piles to test another person and bigger piles, not to shrink the range. Honest limit: the curve uses today's spread; with 17 piles that spread itself is still uncertain.

## Slide 14
What we would do next
IMPROVEMENTS
1 Hand-count piles with markers
Our 3 hand-counted batches had no markers: count again with the markers for a clean detector error.
2 Measure with and without hulls
Shows how much the hulls add; we only measured seeds with hulls.
3 Better scale, and check rounding
A 0.01 g scale shows seed-to-seed weight; coins of known weight show if the scale rounds or cuts off.
4 Coin, card or A4 as ruler
Build and test them, so no user needs our printed sheet.
5 Other crops and seed lots
Per crop: measure grams per seed and the typical seed length on about 10 piles.
6 Use a checklist while working
The procedure was written, but steps were missed when it was not at hand.
Main lesson: measure every variable, then put the result where the user meets it: in the procedure and in the app.
Notes: Six improvements, most of them cheap. The last one comes from Jia's experience: a written procedure only works if it is in front of you while you work; in the app it now is.

## Slide 15
The six course tasks, and the live demo
SUMMARY
Task | Where | Answer in one line
1 Plan the collection | Slides 3 to 5 | Procedure version 3; every rule from a measured problem
2 Feature and number of samples | Slides 8 and 13 | Count of sunflower boxes; about 10 piles
3 Bounds and error propagation | Slide 9 | ±8.7 % for one photo; the photo is not the main error
4 Team-mate repeats | Slide 10 | Jia: 9 of 9 piles inside the bounds
5 Report | This deck and the repository | All numbers can be rebuilt from the code
6 Deployment | Now: live demo | You take a photo with your phone, following the instructions in the app
Demo
Your phone, our app: the result shows the weight, its range, and one light with one sentence. Try one photo with the marker sheet and one without.
Notes: Map from the six course tasks to the slides. Then the demo: CNH takes the photo themselves, following the instructions on the screen.

## Slide 16
Sources and files
APPENDIX
Repository: github.com/HadiNasooti/cnh-sunflower-weight (code, data, results)
Procedure version 3: docs/group/PROCEDURE.md; all variables: docs/group/VARIABLES.md
Results per photo and per pile: analysis/results/2026-10-22_analysis/ (per_photo.csv, per_pile.csv)
Business case: analysis/business_case.py; seeds as ruler: analysis/seed_scale_test.py
App checks: detkit/quality.py; checked on all 59 photos by analysis/validate_light.py
Labour cost: Eurostat, hourly labour costs 2024 (Belgium 48.2 euro per hour)
Bank card size: ISO/IEC 7810 ID-1
Notes: Everything in this talk can be reproduced from the repository.