## Slide 1
CNH DATA COLLECTION PROJECT
From sunflower seeds
to a weight estimate
Designing a repeatable photo-based measurement process
Hadi Nasooti & Jia • KU Leuven • October 2026
Draft report: evidence, uncertainty, limitations and next steps
MEASURE • TEST • IMPROVE

## Slide 2
The story in one slide
OVERVIEW
2
Sunflower group • CNH Data Collection project • Draft for review
Goal
Estimate sunflower-seed pile weight from a photo using a provided detector.
Best feature
Count boxes classified as sunflower × calibrated grams-per-seed constant.
Current evidence
8 original piles (10–24 g), teammate repeat and five exploratory larger piles.
Key findings
• 0.05294 g/seed — calibrated on the original 8 piles.
• ±10.0% — 95% prediction interval for one new photo in the tested setup.
• 4.0% — relative spread after image-scale standardisation.
• 17–36% fewer detections when seeds touched.
Standardise the image and procedure before trusting the number.

## Slide 3
Why estimate weight from a photo?
PROBLEM
3
Sunflower group • CNH Data Collection project • Draft for review
1 Spread
Separate seeds on a plain white background
›
2 Photograph
Markers visible; top-down and level
›
3 Detect
Count sunflower-labelled boxes
›
4 Estimate
Count × calibrated constant
Client need
A fast estimate with a defensible uncertainty range—not a perfect count of every seed.
Course focus
Data-collection design, measured uncertainty and justified conclusions—not retraining the detector.

## Slide 4
Plan and procedure
METHOD
4
Sunflower group • CNH Data Collection project • Draft for review
Design principles
• One seed lot, one white background and the same balance.
• Cover a range of pile weights; unique IDs and collector/device recorded.
• Focus on spacing, scale/height and detector behaviour.
• Take a second photo after moving the phone away and back.
Procedure controls
• TARE before every weighing; record before and after.
• No seed may touch another; keep pile compact.
• Two 50 mm markers flat, fully visible, ≥3 cm from seeds.
• 1× main camera, top-down, about 40 cm; phone level.
• Label note photographed separately; no notes, hands or objects in seed photos.
Why these rules?
Each responds to a measured problem: zero drift, missed touching seeds, changing scale, false boxes and inconsistent framing.

## Slide 5
What data did we collect?
DATASET
5
Sunflower group • CNH Data Collection project • Draft for review
Pilot • Hadi • 17 Oct
Initial tests: a 25 g pile, repeated/touching layouts, and three hand-counted batches of 200 seeds.
Joint camera comparison • 19 Oct
Both team members used the same pile with both phones to explore camera/person differences (Gauge R&R design).
Main collection + procedure repeat • 19–21 Oct
Hadi collected P01–P08 on 19 Oct. Jia followed the same written procedure for Task 4 on 21 Oct (P01–P04), then collected P09–P13 as exploratory larger piles.
18 new photo rows
Appended to samples.csv
• The original calibration and ±10% prediction interval use Hadi's 8 piles in the 10–24 g range.
• Jia's Task 4 uses another phone/person; it is a procedure repeat, not automatically a new calibration.
• P09–P13 extend the observed weight range, but remain exploratory until detection results and validation are analysed.
P14 and P15 were not completed; they are not counted as measured samples.

## Slide 6
Errors we could measure directly
FINDINGS
6
Sunflower group • CNH Data Collection project • Draft for review
Controlled tests
Touching seeds (pilot)
~32% fewer
Touching seeds (main)
~17% fewer
Detector bias on batches
~0.8%
Balance error at 17 g
1.7%
Zero drift
Without fresh TARE, the coin check read +1 g; after TARE, 47.0 g read 47 g.
Repeat weighing
A 25 g pile read 25 g in five lift-and-replace weighings; no variation visible at 1 g resolution.
False positives
Boxes appeared on ruler digits, handwriting and trousers. Counting sunflower boxes only reduces this risk.
A 1 g display step limits precision even when repeated readings look stable.

## Slide 7
Feature choice: count sunflower boxes
MODEL
7
Sunflower group • CNH Data Collection project • Draft for review
Candidate feature evidence • 8 piles
Feature
r
Relative spread
All boxes count
0.990
3.7%
Sunflower boxes count
0.989
4.0%
Sunflower box area (mm²)
0.985
5.4%
Sunflower box area (px²)
0.900
11.6%
Mean box area (px²)
−0.271
35.7%
Chosen model
Estimated weight = sunflower-box count × 0.05294 g/seed
Why not pixel area?
Pixel area changes with camera height. Marker-calibrated mm² is better, but count has the lowest relative spread among useful candidates.
Why sunflower-only?
It avoids false boxes from other classes on notes and markers.
High correlations partly reflect the wide weight range; relative spread is more useful for comparing features.

## Slide 8
Major improvement: standardise image scale
CALIBRATION
8
Sunflower group • CNH Data Collection project • Draft for review
Photos as taken
Grams per seed: 0.0542 mean
Relative SD: 5.9%
Correlation with mm/px: +0.63
Mean A–B difference: 3.0%
Fixed scale = 0.110 mm/px
Grams per seed: 0.0529 mean
Relative SD: 4.0%
Correlation with mm/px: +0.04
Mean A–B difference: 1.2%
As taken
5.9%
Fixed scale
4.0%
Interpretation
Marker-based scaling reduces the camera-height effect and makes counts more comparable. The fixed scale is built into the app.
With fixed scale, the 12 MP test stayed within about 2% of the full-resolution count.

## Slide 9
What does ±10% mean?
UNCERTAINTY
9
Sunflower group • CNH Data Collection project • Draft for review
95% prediction interval
For one new photo in the tested setup, the true weight is expected to fall within the interval about 19 times out of 20.
−10%
Estimate
+10%
Calibration basis
8 original piles, 10–24 g; constant = 0.05294 g/seed.
Bound itself is uncertain
With only 8 piles, the true spread could plausibly be 0.66–2.0× the estimate.
15-pile projection
With the same spread, the interval might be about ±8.8%. This is hypothetical; P14/P15 were not completed.
Do not present ±10% as a universal guarantee for other phones, seed lots or weights.

## Slide 10
Error budget: explaining the 4% spread
UNCERTAINTY
10
Sunflower group • CNH Data Collection project • Draft for review
Relative standard errors at mean pile weight 17 g
Balance
1.7%
Detector
1.0%
Unexplained remainder
3.4%
Observed spread (top-down)
4.0%
Variance shares
Balance 18% • Detector 7% • Unexplained 75%
Not measurable yet
Three 200-seed batches all read 11 g at 1 g resolution; seed-to-seed variation could not be resolved.
Interpretation
Most variation is not explained by the measured stages.
Remainder = √(4.0² − 1.7² − 1.0²) ≈ 3.4%.

## Slide 11
Teammate repeat: useful but not clean yet
REPEATABILITY
11
Sunflower group • CNH Data Collection project • Draft for review
• Jia used an iPhone 14 (1×); original main collection used Hadi's iPhone 15 Pro.
• Task 4: P01–P04, two photos per pile; 8 records.
• P09–P13: five additional piles, two photos each.
• All 18 new photo rows have been appended to samples.csv.
Task 4 weighing notes
Pile
Before
After used
Difference
P01
10 g
11 g
+1 g
P02
14 g
12 g
−2 g
P03
Not numeric
18 g*
Unresolved
P04
22 g
23 g
+1 g
*P03 numeric before/after readings not recorded.
Deviations to disclose
Sticker notes remain visible; photos were not retaken. Camera height varied about 35–45 cm. P02 differs by 2 g before/after and needs checking.

## Slide 12
Exploratory larger piles and limits
LIMITATIONS
12
Sunflower group • CNH Data Collection project • Draft for review
After-weights recorded for P09–P13
27
P09
28
P10
29
P11
32
P12
34
P13
Observed range extends to 27–34 g, but these data have not been used to refit or validate the model.
P14 / P15
Not completed. A preliminary visual check suggested the pile might exceed the image area at the allowed height; no formal fit test was done.
What we can claim
The practical stopping point is a qualitative observation, not a verified maximum imageable weight.
Range limitation
The original ±10% interval is calibrated for 10–24 g. Larger samples should be labelled exploratory until the model is re-evaluated.

## Slide 13
What we would change next time
IMPROVEMENTS
13
Sunflower group • CNH Data Collection project • Draft for review
1 • Measure with and without hulls
Sunflower seeds may need a hulled-versus-unhulled weight comparison. We only measured seeds with their hulls this time because dehulling every sample was too time-consuming.
2 • Use a step-by-step checklist
The written procedure was already standardised. The issue was that the operator did not consult it while working and missed Step 6. Next time, check off each step as it is completed.
3 • Count seeds in validation samples
We did not manually count the seeds in the main piles because there were too many. In a future validation subset, count a manageable sample to compare detector counts with ground truth.
4 • Fix the camera height
We measured height approximately with a ruler but had no fixed stand. A simple stand or height jig would make the camera-to-table distance repeatable.
5 • Analyse the cross-phone repeat
Use the 19 Oct same-pile, two-person/two-phone comparison to separate repeatability from operator and device effects, and report the measured differences.
6 • Extend the tested range carefully
Analyse P09–P13 separately first; only refit the calibration and prediction interval after checking counts and validating performance at larger weights.
Main lesson: a good written protocol is not enough on its own—operators need a practical habit of checking each step as they go.

## Slide 14
Sources and final checks
APPENDIX
14
Sunflower group • CNH Data Collection project • Draft for review
• Repository: https://github.com/HadiNasooti/cnh-sunflower-weight
• Procedure: docs/group/PROCEDURE.md (v2, 19 Oct 2026).
• Analysis and error budget: docs/group/STATUS_AND_PLAN.md, sections 3b–4b.
• Measurement index: data/samples.csv; notes: docs/group/lab_log.md.
• CSV has 51 data rows after adding the 18 new photo rows.
Before final submission
Confirm P02's 14 g → 12 g change; ask Hadi whether Task 4 must be repeated; run detector analysis on Jia's photos if possible; add actual cross-person/cross-phone Gauge R&R results if completed.